## Slide 1
In-Cabin Passenger Detection using millimeter-Wave Radar
FYDP Final Defence EE SEECS NUST Main Campus
1
Team Members: Raiha Raees, Areeba Mehboob, Syeda Zayra Batool
Advisor: Dr. Nosherwan Shoaib, Dr. Hammad M. Cheema
Final Year Project

## Slide 2
  Introduction
  Problem Statement
  Literature review
  Objectives
  Methodology
  Implementation
  Results
  Demo Video
  Conclusion
Table of Content
FYDP Final Defence EE SEECS NUST Main Campus
2

## Slide 3
FYDP Final Defence EE SEECS NUST Main Campus
3
Problem Statement
An examination of media reports about the 938 pediatric vehicular heatstroke deaths for a 25-year period (1998 through 2022) shows the following circumstances:
- 52.61% - Forgotten by caregiver (496 children)
- 25.29% - Gained Access on their own (237)
- 20.28% - Knowingly left by caregiver (190)
- 1.81% - Unknown (17)
More than half of the deaths (54%) are children under 2 years of age.
https://noheatstroke.org/original/index.html

## Slide 4
FYDP Final Defence EE SEECS NUST Main Campus
4
SafeAuto is a new IoMT device for accurate non-contact breathing rate measurement to ensure child safety in a vehicle.
SafeAuto
This device uses a 60 GHz short range pulsed radar.
The estimated breathing rates are communicated to the user (parent/guardian) over wifi.

## Slide 5
Ref. # | Paper | Radar | Frequency | Subject Distance | %Error (Breathing Rate) | Methodology
[2] | (S. Wang, 2015) | FMCW | 80 GHz | 1m | 6.89% | FFT
[3] | (M. Alizadeh, 2019) | FMCW | 77 GHz | 1.7m | 6% | FFT
[4] | (Zhicheng Yang, 2016) | CW | 60 GHz | 1m | 2% | FFT
FYDP Final Defence EE SEECS NUST Main Campus
5
Literature Review

## Slide 6
FYDP Final Defence EE SEECS NUST Main Campus
6
Objectives
This project aims to design an efficient system with low false-positive and false-negative rates having the objectives:
  To perform detection of any in-Cabin passengers.
  To distinguish between children and adults.
  To alert the owner or the guardian if a child is accidentally left behind in the car so any accidents can be prevented.
  To promote child passengers’ health and safety, aiming towards achieving SDG 3.

## Slide 7
FYDP Final Defence EE SEECS NUST Main Campus
7
Block Diagram
FEATURE EXTRACTION
FEATURE SELECTION
CLASSIFICATION
NOTIFICATION
PREPROCESSING
DATA ACQUISITION
3
4
5
6
2
1
Using filters to extract frequency components.
Calculating Breaths Per Minute to perform classification.
Data passes through ML classifier for detection
A message will be sent to the caregiver of the child that your child is locked in car.
Reshaping of data from H5 file and extracting inphase and quadrature components
Storing Breathing Data from xm112 for preprocessing

## Slide 8
Visual studio
Usb cable
XM112 radar module
FYDP Final Defence EE SEECS NUST Main Campus
8
Hardware & Tools
Lens
Colab

## Slide 9
FYDP Final Defence EE SEECS NUST Main Campus
9
Methodology
  Our prototype first receives pulse coherent waves reflected back from the passenger.
  These signals are then processed to compute breathing rate.
  The breathing rate is classified as as adult’s or a child’s using ML model.
  Visual Studio is utilized for signal processing, while Twilio is integrated with Visual Studio to facilitate user notifications.

## Slide 10
FYDP Final Defence EE SEECS NUST Main Campus
10
Implementation:
Data Acquisition (Presence Detection)
No object
With object

## Slide 11
FYDP Final Defence EE SEECS NUST Main Campus
11
Data Acquisition (IQ)
Amplitude and Phase of Radar Data

## Slide 12
FYDP Final Defence EE SEECS NUST Main Campus
12
Implementation:
Data Collection at Fazilia Public School and NUST

## Slide 13
FYDP Final Defence EE SEECS NUST Main Campus
13
Hardware Implementation
XM112
radar module
Lens

## Slide 14
FYDP Final Defence EE SEECS NUST Main Campus
14
Results - Signal Processing
  We initially processed the incoming signal into breathing rate using Google Colab.
  The results of which are shown as:
  For verification purposes, we manually counted the beathing rate of six subjects and the value calculated using radar was shown to give 95.48% accuracy.
Results - Machine Learning
  After putting the calculated respiration rate through the trained KNN classifier, Colab gives us the results in the following form:

## Slide 15
FYDP Final Defence EE SEECS NUST Main Campus
15
GUI
  Here is the graphical user interface for SafeAuto:
Text Alert
  Twilio is used via visual studio for text alert.

## Slide 16
Subject | Breathing rate from radar | Breathing rate from manual counting | Percentage accuracy
1 | 20.68 20.46 | 20 19 | 96.6 92.315
2 | 19.85 18.97 | 19 19 | 95.526 99.842
3 | 16.21 18.23 | 17 18 | 95.352 98.72
FYDP Final Defence EE SEECS NUST Main Campus
16
Percentage Accuracy
Subject | Breathing rate from radar | Breathing rate from manual counting | Percentage accuracy
4 | 14.57 20.21 | 14 21 | 95.928 96.238
5 | 20.67 16.51 | 19 17 | 91.210 97.11
6 | 17.48 15.39 | 16 16 | 90.750 96.188

## Slide 17
FYDP Final Defence EE SEECS NUST Main Campus
17
Demonstration Pictures and Video
Link to the Demo Video:
Click here

## Slide 18
Sr No. | FYDP Deliverables | Status
1 | Final Report | Yes
2 | Final Presentation slides | Yes
3 | Poster (A1 size) | Yes
4 | Plagiarism report | Yes
5 | Demo Video | Yes
FYDP Final Defence EE SEECS NUST Main Campus
18
FYDP Deliverables Upload Status (PMS)

## Slide 19
FYDP Final Defence EE SEECS NUST Main Campus
19
References
[1] Fact Sheet - Heatstroke Deaths of Children in Vehicles. (n.d.-b). https://noheatstroke.org/original/index.html
[2] Wang, S., Pohl, A., Jaeschke, T., Czaplik, M., Köny, M., Leonhardt, S., & Pohl, N. (2015). A novel ultra-wideband 80 GHz FMCW radar system for contactless monitoring of vital signs. https://doi.org/10.1109/embc.2015.7319509
[3] Alizadeh, M., Shaker, G., De Almeida, J. C. M., Morita, P. P., & Safavi-Naeini, S. (2019). Remote Monitoring of Human Vital Signs Using mm-Wave FMCW Radar. IEEE Access, 7, 54958–54968. https://doi.org/10.1109/access.2019.2912956
[4] Yang, Z., Pathak, P. H., Zeng, Y., Liran, X., & Mohapatra, P. (2016). Monitoring vital signs using millimeter wave. https://doi.org/10.1145/2942358.2942381

## Slide 20
FYDP Final Defence EE SEECS NUST Main Campus
20
Thank You!